## Slide 1
Linear Stability of Channel Flow
with Melting Top and Bottom Walls
Summer Research Project
Mohd Izhan Khan
Fluid Dynamics · Hydrodynamic Stability
Notes: Welcome. 8-week summer project: linear stability of channel flow with melting walls. Overview of the journey from classical Orr-Sommerfeld theory to the coupled phase-change problem.

## Slide 2
What is Stability?
Definition: A system is stable if infinitesimal perturbations about its equilibrium state remain bounded or decay in time.
↓
Stable
Perturbation decays
and flow returns to
its equilibrium state
→
Neutral
Perturbation neither
grows nor decays —
neutral stability curve
↑
Unstable
Perturbation grows,
leading eventually to
turbulent transition
Notes: Establish the language: stable/neutral/unstable. Im(c) is the key scalar that tells us everything about linear stability.

## Slide 3
Equilibrium States: The Pendulum
Classical mechanics offers the most intuitive model for stability:
Stable
Equilibrium
Unstable
Equilibrium
Notes: The pendulum analogy makes stability concrete. At high Re the inertial terms overwhelm viscous damping — analogous to the inverted pendulum losing its restoring force.

## Slide 4
Hydrodynamic Stability
Fluid flows also respond to perturbations (wall roughness, vibrations, inlet disturbances)
Laminar Flow
Smooth, ordered motion. Perturbations decay. Characteristic of low Reynolds-number regimes.
Transition
Perturbations begin to grow. Coherent structures (rolls, streaks, Tollmien-Schlichting waves) emerge.
Turbulent
Chaotic disordered motion. Dramatic increase in mixing, drag, and heat transfer.
[ Insert: s4.jpeg ]
Notes: Bridge from solid mechanics to fluid flows. The Reynolds number is the key control parameter — low Re is laminar, high Re leads to turbulence.

## Slide 5
Phenomenological Example: Kelvin-Helmholtz Instability
Arises at the interface of two fluid layers moving at different speeds:
Mechanism Velocity shear at the interface creates a pressure difference. Small bumps are swept downstream and amplified, rolling into characteristic spiral vortices. Where it occurs • Ocean-atmosphere boundary layer
• Cloud formations in wind shear
[ Insert: kh.jpeg ]
Notes: KH instability is the most visually striking example of hydrodynamic instability. The rolling pattern appears in clouds, oceans, and Jupiter's atmosphere.

## Slide 6
Plane Poiseuille Flow
The unperturbed base state: pressure-driven flow between two infinite rigid parallel plates.
Base Velocity Profile
U(y) = 1 − y², −1 < y < 1
Domain: Walls at y = ±1 (half-channel width h = 1)
Driving: Constant pressure gradient −dP/dx > 0
Profile: Parabolic, maximum U_max = 1 at y = 0
Re = U_max h/ν — controls the flow stability
[ Insert: pp.jpeg ]
Notes: Poiseuille flow is the canonical base state. It's an exact solution of the Navier-Stokes equations. Our stability analysis asks: is this base state robust?

## Slide 7
Introducing Perturbations
Decompose the flow into base state + infinitesimal perturbation, then assume normal mode solutions:
u(x,y,t) = U(y) + ε û(x,y,t), p(x,y,t) = P(x) + ε p̂(x,y,t), ε ≪ 1
Normal Mode
ẇ(x, y, t) = w(y) · e^{iα(x − ct)}
α: Real wavenumber — sets the spatial scale of the perturbation in x
c = cᵣ + icᵢ: Complex wave speed: real part = phase speed, imaginary part = growth/decay rate
cᵢ > 0: Exponential growth — the flow is linearly UNSTABLE to this mode
cᵢ < 0: Exponential decay — the flow is linearly stable to this mode
Notes: The normal mode (Fourier mode in x) reduces the linearized PDE to an ODE in y, leading to an eigenvalue problem for c.

## Slide 8
Linearizing the Equations
Substitute perturbed state into 2D Navier-Stokes; discard all O(ε²) terms:
Continuity (incompressibility)
∂û/∂x + ∂v̂/∂y = 0
x-Momentum
∂û/∂t + U ∂û/∂x + v̂ U' = −∂p̂/∂x + (1/Re)(∂²û/∂x² + ∂²û/∂y²)
y-Momentum
∂w/∂t + U ∂w/∂x = −∂p̂/∂y + (1/Re)(∂²w/∂x² + ∂²wType equation here./∂y²)
U' = dU/dy is the base-state shear. Nonlinear terms (û∂û/∂x, etc.) are O(ε²) and discarded.
Notes: The linearization step is what makes the problem tractable. It converts nonlinear PDEs into a linear eigenvalue problem.

## Slide 9
The Orr-Sommerfeld Equation
Fourth-order ODE governing linear stability of all parallel shear flows:
(D² − α²)² w = iα Re [ (U − c)(D² − α²)w − U'' w ]
Left — Viscous Term
(D² − α²)² w
Fourth-order operator representing viscous dissipation. Acts to damp perturbations at all scales.
Right — Inertial Terms
iαRe [(U−c)(D²−α²)w − U''w]
Convection by the base flow + base-state shear. The U'' term (curvature) can destabilize the flow.
D ≡ d/dy · Re = Reynolds number · α = wavenumber · c = complex wave speed
Notes: The Orr-Sommerfeld equation was derived independently in 1907-1908. It is the cornerstone of hydrodynamic stability theory. Note: for inviscid flow (Re→∞) it reduces to the Rayleigh equation.

## Slide 10
Constraining the Flow
The 4th-order OS equation requires four boundary conditions (two per wall):
At both rigid walls ( y = +1 and y = −1 ):
w(±1) = 0
No-penetration — fluid cannot pass through the solid wall
Dw(±1) = 0
No-slip — tangential velocity perturbation vanishes at the wall
Physical Interpretation
Four conditions (2 walls × 2) constrain the 4th-order OS problem. Together they define a homogeneous boundary-value problem whose non-trivial solutions exist only for particular complex eigenvalues c = cᵣ + icᵢ. The totality of these eigenvalues constitutes the Orr-Sommerfeld eigenspectrum.
Notes: Four BCs for a 4th-order ODE — this is a well-posed Sturm-Liouville-type problem. The homogeneous problem only has non-trivial solutions for special eigenvalues c.

## Slide 11
Interpreting the Eigenvalues
The solution c = cᵣ + icᵢ encodes all temporal stability information:
ŵ ∝ e^{iα(x − ct)} = e^{iα(x − cᵣ t)} · e^{α cᵢ t}
⬆
cᵢ > 0
Linearly UNSTABLE
Amplitude grows exponentially as e^{αcᵢt}. Flow transitions to turbulence.
→
cᵢ = 0
Neutrally Stable
Constant amplitude. Perturbation propagates without growth or decay. Marks the stability boundary.
⬇
cᵢ < 0
Linearly Stable
Amplitude decays as e^{αcᵢt} → 0. Laminar flow is robust against small disturbances.
Notes: The imaginary part of the eigenvalue is the decisive quantity. Most modes in Poiseuille flow are stable; only a narrow band in (α,Re) space is unstable.

## Slide 12
Critical Eigenvalue Spectrum
Rigid-wall benchmark: the Orr-Sommerfeld spectrum confirms the classical critical parameters.
[ Insert: eigen_spectra.png ]
Critical Parameters : RED DOT
Reᶜ = 5772.22
Critical Reynolds number
αᶜ = 1.02056
Critical wavenumber
At Re = Reᶜ the Tollmien-Schlichting (TS) wave first becomes unstable. For Re < Reᶜ all modes are damped.
Notes: This benchmark replicates the result first computed accurately by Orszag (1971). It validates the Dedalus EVP solver before tackling the harder melting-wall problem.

## Slide 13
Fluid Displacement Profiles
[ Insert: eigen_func.png ]
Mode Classification
Tollmien-Schlichting
Critical TS wave. Concentrated near walls. First to become unstable at Reᶜ.
Centre Modes
Peak amplitude at channel centre y = 0. Always stable for Poiseuille flow.
Damped Wall Modes
Highly decaying, confined close to walls. Require high N for accurate resolution.
Notes: The TS mode is the physically relevant one for channel flow transition. The centre modes are spurious in the sense that they don't lead to turbulence in this configuration.

## Slide 14
Neutral Stability Curve
Maps the stability boundary in wavenumber α vs Reynolds number Re space (cᵢ = 0 contour):
[ Insert: neutral_curve.png ]
Reading the Curve :
Inside curve
Unstable region
(cᵢ > 0)
Outside curve
Stable region
(cᵢ < 0)
Critical point ★
Re ≈ 5772, α ≈ 1.02
Notes: The neutral curve is the primary deliverable of classical stability theory. For Re below 5772 all wavelengths are stable — but the basin of attraction shrinks as Re increases.

## Slide 15
The Next Step: Melting Boundaries
What happens when the rigid walls melt? The interface y = ±h(x,t) becomes dynamic.
Stefan Condition:
St · ∂h/∂t = κₛ (∂Tₛ/∂y)|_{y=h⁺} − κₗ (∂Tₗ/∂y)|_{y=h⁻}
Hydrodynamics
Perturbed NS equations with deforming boundaries. Interface h(x,t) couples into the kinematic and stress BCs.
Heat Transfer
Liquid and solid temperature fields Tₗ, Tₛ governed by advection-diffusion in their respective domains.
Phase Change
Stefan condition links melt-rate to heat flux balance. Opens new instability pathways absent in rigid-wall flow.
Key question: does melting stabilize or destabilize the channel flow — and through which physical mechanism?
Notes: The main project goal. Adding phase change converts the fixed-domain OS problem into a free-boundary eigenvalue problem. The Stefan number St and conductivity ratio are new control parameters alongside Re.